USB Play Box

Overview

USB Play Box is transport stream play box which has USB2.0 interface and PC software, providing a complete API interface, which makes it an ideal hardware development platform for digital TV equipment. It is mainly used for sending transporting stream date stored in computer hardware in specific bit-rate, and it can be used as well as digital TV stream generator.

Features

- Direct power access through USB interface, no need of external power supply

- Automatic calculation of bit-rate, manually set the playback bit-rate

- 8M bytes of super high-speed buffer memory to ensure the stability of high bit-rate output

- Aluminum alloy shell, small size, easy to carry

- Support secondary development

Technical Specification

| USB Interface | USB2.0 |
| --- | --- |
| ASI | 2xBNC interface |
| General Features | Size | 93mm×153mm×42mm |
|  | Temperature Range | 0~45°C (Operation); -20~80°C (Storage) |
|  | Power | 100-240VAC, 50Hz, 25W |